## Slide 1: Connect Four
C2C John Terragnoli

## Slide 2: Embedded System
I built an embedded system which acts as a Connect Four Game for 2 players.
Use buttons on computer chip or remotes to move and drop pieces
Game displayed on standard TV or monitor via HDMI cable

## Slide 3: Need
Board Game companies are eager to keep up with technological advances. Digitalizing them to be played with common-house items allows Board Games to stay relevant.

## Slide 4: Level-0 Description
Inputs | Remote IR signal, directional and select buttons are required.
Outputs | A monitor will display a grid of the game. Different squares in the grid will be filled in with the appropriate color when a player chooses to place a piece there.
Behavior | Should decode the IR signals, determine if it is a viable move or not, determine which rectangle should be lit up, determine if the player has won the game or not, and end the game if it has. Required functionality is to get the program to work using the buttons on the FPGA. B Functionality is to use one remote to play the game. A Functionality is to have two remotes, one for each player, to play the game.

## Slide 5: Videos

## Slide 6: Level-1 Architecture

## Slide 7: Control Unit

## Slide 8: Datapath

## Slide 9: Idea Datapath
Note: Numbers reference order of creation

## Slide 10: 1: BRAM to Video
Drawing Basics
Counters used to count through row and column of pixels on display
Based on the pixel address, a specific color is sent to that pixel on the screen. In total an image is drawn

## Slide 11: BRAM to Video
Screen Dimensions

## Slide 12: BRAM to Video
Initial, Static Board

## Slide 13: BRAM to Video
whatOn: 2 bits long, designates color of pixel being referenced
00: black (empty)
01: blue
10: red

## Slide 14: BRAM to Video
Indexes Labeled

## Slide 15: BRAM to Video
Every (row,column) coordinate is associated with a (rowIndex, colIndex).
RDADDR <= “00” & rowIndex & colIndex
Each address associated with a color
When “Video” is writing to a specific (row, column) address, the color store at specific index is written to that pixel

## Slide 16: BRAM to Video

## Slide 17: 2: Updating BRAM
Marker needs to be show at the top so users know which column they’re using
Must fill according to the rules of the game
Colors need to alternate

## Slide 18: Updating BRAM
Marker:
  10 possible locations which correspond with the column indexes
  NOT stored in BRAM
  Marker index can be changed with left and right button presses.
  When “Video” references a pixel within the index location, yellow is drawn to that pixel

## Slide 19: Updating BRAM
Create 10 “fill” signals; one for each column.
The fill signals keep track of which row the program should write to next
As the user is choosing the column, the program is referencing the row to write to if the user finalizes that row. Then the color switches from red to blue.

## Slide 20: Updating BRAM
Fill signals

## Slide 21: Updating BRAM debugging
Debouncing
  To fix this issue, the top button must be pressed in between either the left, center, and right buttons.
Overwriting
  An enable/disable signal needed to be created from the FSM so that after a move was made, other columns were not changed

## Slide 22: 3: Winning Logic
Second BRAM created
Checked after every move was made
FSM was paused during this process
Only boxes around the spot a piece was just placed were checked.

## Slide 23: Winning Logic
Identical BRAM created
  Same writing input signals as the first BRAM
  Reason: it is impossible to read from different indexes at the same time. Need to read for visual and winning logic.

## Slide 24: Winning Logic
Ripping BRAM:
  Need to save the values of the surrounding boxes (21) in separate signals to compare them at the same time.
  Unfortunately, can only read from BRAM serially
  Mini FSM was built to go through all of these addresses and obtain the data held there.
  Relative addressing used
  Pause master FSM during process

## Slide 25: Winning Logic
Relative Addressing:

## Slide 26: Winning Logic
13 possible winning combinations of boxes:
  4 across
  8 diagonal
  1 vertical
Checked with combinational logic

## Slide 27: Winning Logic
Displayed on the Screen

## Slide 28: Winning Logic
Testbench
Red signals
Got ripped
From BRAM
And stored in
Signals

## Slide 29: 4: Decoding the IR Signal
Long highs are 1’s, short highs are 0’s.
Timing determined using counters and clock cycles.
Shift register used to collect the bits as they were translated.
Compiled bits were converted into button presses so game could be played as before.

## Slide 30: Decoding IR Signal
Start bit, short highs, long highs.

## Slide 31: Decoding the IR Signal
Using logic analyzer the signals were manually decoded:
Left: | 00000000111111110101000010101111 | 00FF50AF
Center: | 00000000111111110000001011111101 | 00FF02FD
Right: | 00000000111111110111100010000111 | 00FF7887
Top | 00000000111111111010000001011111 | 00FFA05F

## Slide 32: Decoding IR Signal
Signal Lengths
 | short high | long high | start bit | 
average = | 0.5440286 | 1.686629 | 4.537029 | (ms)
std_dev | 0.0022839 | 0.009391 | 0.011942 | (ms)
Clock Cycles Upper | 55441 | 174475 | 459370 | 
Clock Cycles Lower | 53158 | 165084 | 447429 | 

## Slide 33: Decoding IR Signal

## Slide 34: Decoding IR Signal

## Slide 35: Decoding IR Signal

## Slide 36: QUESTIONS?